## Slide 1: ISAR Test Matrix
Greg Showman
25 June 2026

## Slide 2
Case # | Number of Ambiguities Having Scatterers | Number of Ambiguities In Image Former | Scatterer Locations | Image Former Grid Density | Angle Rate | Noise | Image Formation Algorithm | Prediction | Results
1 | 1 | 1 | On-Grid | Critical | Constant | None | BP-EQ | Good 0-1 image | 
2 | 1 | 1 | On-Grid | Critical | Constant | None | OMP | Good 0-1 image | 
3 | 1 | 1 | On-Grid | Critical | Accelerating | None | BP-EQ | Good 0-1 image | 
4 | 1 | 1 | On-Grid | Critical | Accelerating | None | OMP | Good 0-1 image | 
5 | 1 | 1 | Off-Grid | Critical | Constant | None | BP-EQ | Good image with sidelobes | 
6 | 1 | 1 | Off-grid | Critical | Constant | None | OMP | Good image with multiple “on” pixels per scatterer | 
7 | 1 | 1 | Off-grid | Oversampled | Constant | None | BP-EQ | Improved interpretability w.r.t. Case 5 | 
8 | 1 | 1 | Off-grid | Oversampled | Constant | None | OMP | Improved match w.r.t. Case 6 | 
9 | 1 | 1 | Off-grid | Oversampled | Accelerating | None | BP-EQ | Same as Case 7 | 
10 | 1 | 1 | Off-grid | Oversampled | Accelerating | None | OMP | Same as Case 8 | 

## Slide 3: Definitions
Number of Ambiguities Having Scatterers: Number of Doppler/Crossrange ambiguities containing one or more scatteres. If just 1, all scatterers are in the “zeroth” ambiguity. Unambiguous Doppler/crossrange extent is defined with respect to the constant angle rate collection case.
Number of Ambiguities In Image Former: The number of crossrange ambiguities represented in the image formation “target grid.”
Scatterer Locations: On the grid or off the grid provided by a critically-sampled image former. If off this grid, scatterer offset from grid is random and uniformly distributed, so that there is no underlying grid.
Image Former Grid Density: Critically-sampled in downrange and crossrange respect to downrange and crossrange resolutions, or oversampled in both dimensions. (Degree of oversampling TBD and may be varied parametrically.)
Angle Rate: During data collection; constant or accelerating.
Noise: Thermal noise level; none or non-zero. (Non-zero level TBD and may be varied parametrically.)
BP-EQ: Backprojection with angle rate equalization. (Brandon successfully implemented this some months ago. Did we call it something else???)
OMP: Orthogonal Matched Pursuit.
Prediction: Brandon, what do you expect to see? “0-1” means pixels will be either off or on.
Results: What you got, and compare/contrast with predictions.